## Slide 1: Minimum Sign Retroreflectivity Requirements Updated August 2012 with compliance date revisions
Notes: <number>
New Retroreflectivity standards were added to the MUTCD in December 2007 and related compliance dates were revised in May 2012.
The standards are a result of many years of research regarding the needs of the drivers – how many have heard about retroreflectivity before?
The intent of the standards are a solution that meets needs of most involved.

## Slide 2: Why Do We Install Signs?
Required by MUTCD?
To help drivers
(including older)
Most are not
Engineering Decision?
YES!
Why?
Notes: <number>
While some signs are required, most are not. The Manual describes application of TCDs (1A.09)
Typically the decision to install a sign is based on Engineering Judgment. The standards/guidance/options come into play to promote uniformity in the application in an effort to help drivers safely navigate (regulate, warn, guide)
Once the decision is made that a sign is needed, the MUTCD requires:
  Same shape and similar color day and night
  Retroreflective or Illuminated

## Slide 3: Night Travel and Crashes
Notes: <number>
Why the big concern?
Only about 25% of travel occurs in dark conditions, but 50% of crashes
The nighttime crash rate is nearly three times that of daytime
Both behavioral (fatigue, alcohol) and engineering contributors to this disparity between nighttime and daytime -- Improving visibility helps everyone
Sources:
Crash Data – NHTSA Fatal Accident Reporting System
VMT – FHWA Highway Statistics

## Slide 4: But, Retroreflectivity Degrades Over Time
Retroreflectivity
When
Do We
Replace
Signs?
Signs Provide Critical Information to Drivers
Notes: <number>
Signs are generally adequate when installed.
Signs degrade with sunlight, weather, environmental damage. Daylight and Nighttime degradation varies.
Do you have a method in place to determine when to replace?

## Slide 5: Final Rule to Establish Min Reto
Published on Dec 21, 2007
  Vol 72, No. 245
Revision #2 of the 2003 Edition of the MUTCD
Effective Jan 22, 2008
Notes: <number>
Not all signs have been adequately maintained
Now there are standards and guidance for all agencies to follow
  Some agencies may already be in compliance, for other agencies this may raise the visbility of their signs

## Slide 6: MUTCD Language Section 2A.08 Maintaining Minimum Retroreflectivity
“Standard:
Public agencies or officials having jurisdiction shall use an assessment or management method that is designed to maintain sign retroreflectivity at or above the minimum levels in Table 2A-3”
Notes: <number>
New Language (standard)
Major change is in Section 2A.08
Centers around a method to maintain retroreflectivity

## Slide 7
Sign Color | Sheeting Type (ASTM D4956-04)  |  |  |  | Additional Criteria
 | Beaded Sheeting |  |  | Prismatic Sheeting | 
 | I | II | III | III, IV, VI, VII, VIII, IX, X | 
White on Green | W* G ≥ 7 | W* G ≥ 15 | W* G ≥ 25 | W ≥ 250; G ≥ 25 | Overhead
 | W* G ≥ 7 | W ≥ 120; G ≥ 15 |  |  | Ground-mounted
Black on Yellow or Black on Orange | Y*; O* | Y ≥ 50; O ≥ 50 |  |  | 
 | Y*; O* | Y ≥ 75; O ≥ 75 |  |  | 
White on Red | W ≥ 35; R ≥ 7 |  |  |  | 
Black on White | W ≥ 50 |  |  |  | 
 The minimum maintained retroreflectivity levels shown in this table are in units of cd/lx/m2 measured at an observation angle of 0.2 and an entrance angle of -4.0.  For text and fine symbol signs measuring at least 1200 mm (48 in) and for all sizes of bold symbol signs  For text and fine symbol signs measuring less than 1200 mm (48 in)  Minimum Sign Contrast Ratio ≥ 3:1 (white retroreflectivity ÷ red retroreflectivity) * This sheeting type shall not be used for this color for this application. |  |  |  |  | 
MUTCD Table 2A.3
Minimum Maintained Retroreflectivity Levels
Notes: <number>
The numbers are also in the MUTCD (this was somewhat controversial)
  The chart is a little complex, so Example 1: a curve warning sign
    black on yellow
    *Type I (eng grade) should not be used
    Any other type okay and should have a yellow retro level of 50 or 75
    (2) Since curve is not text or fine symbol, should meet 50
    Black not retroreflective, so don’t have to measure it.
  Example 2: Stop Sign
    Any type sheeting meets initially
    Both white and red have to meet retro levels: White >35, Red>7
    (3) Need contrast ratio > 3:1 (e.g. red=20, white must >60)

## Slide 8: Methods to Maintain Retro
Visual Nighttime Inspection
  Calibration Signs
  Comparison Panels
  Consistent Parameters
Measured Sign Retro
Expected Sign Life
Blanket Replacement
Control Signs
Future Method Based On Engineering Study
Combination Of Any
Notes: <number>
Methods Intro
So those are the numbers you need to meet, but remember the requirement is to have a method that maintains those minimums.
The rule provided much versatility – many methods are available
Basics are in the brochure (http://safety.fhwa.dot.gov/roadway_dept/retro/sa07020/sa07020.pdf),
Research details are in the “Methods Report” on-line at FHWA nighttime visibility site.
Each method has some advantages and disadvantages that should be considered. Combining methods can help minimize the concerns/disadvantages.
Keep in mind the goal is to have visible signs that at least meet the needs of drivers during nighttime.

## Slide 9: MUTCD Language Section 2A.08 Maintaining Minimum Retroreflectivity
“Support:
Compliance… is achieved by having a method in place and using the method to maintain the minimum levels established in Table 2A-3. Provided that… a method is being used, an agency would be in compliance… even if there are some individual signs that do not meet the… levels at a particular point in time.
Notes: <number>
This support statement helps to limit an agency’s liability: compliance is by implementing a maintenance method, even if some signs do not meet levels at a particular time.
It is not meant as an easy out: the maintenance method must be designed to maintain the minimum requirements fro sign retroreflectivity.

## Slide 10: Exempt Signs
Parking/Standing/Stopping
Walking/Hitchhiking
Adopt-A-Highway
Blue or Brown Backgrounds
Exclusive Use of Bikes
or Peds
Note: Must still meet other
requirements in MUTCD
(inspections, retroreflective,
etc,)
Notes: <number>
Several signs are exempted. The research for blue and brown retroreflectivity has been completed since the standards were adopted. Report FHWA-HRT-08-029 provides minimum recommended retroreflectivity levels for blue and brown signs.

## Slide 11: Compliance Date Final Rule
May 14, 2012
Eliminated 46 items
Revised 4 others items
Safety related compliance dates maintained (8)
Revision #2 of the 2009 MUTCD
Notes: The final rule also adds a new Option statement exempting existing historic street name signs within a locally identified historic district from
the Standards and Guidance of Section 2D.43 regarding street sign color, letter size, and other design features, including retroreflectivity.
2009 MUTCD Revision 1 deals with change in Engineering Judgment definition – not part of this presentation
<number>

## Slide 12: Updated Sign Retroreflectivity Compliance Dates
Notes: <number>
The dates for having a method selected and in use was extended 2.5 years. Guide signs have been removed from the first compliance dates…however, they are to be added to an agency's management or assessment method as resources allow.
The compliance dates for signs below the minimums have been removed …. without these “target” compliance dates, each agency must prioritize and justify their schedule of sign replacement. Signs identified through an agency‘s maintenance method as being below the minimum established retroreflectivity levels have exhausted their useful service life and need to be replaced because they do not meet the needed function of being adequately visible at night.
Agencies are expected to prioritize replacement of wornout signs based on engineering considerations, similar to other traffic control devices.

## Slide 13: Why were guide signs removed from compliance dates ?
Regulatory and warning signs constitute the highest priority for assessing retro of existing signs
Including guide signs would increase the economic burden
Section 2A.08 still requires a method for all signs, including guide signs
Notes: <number>

## Slide 14: When do I have to replace my worn out signs?
Agencies are expected to prioritize replacement of these signs based on engineering considerations, similar to other traffic control devices.
It is expected that the use of the assessment or management method would serve to identify and program the replacement of signs that are found to or expected to be below the minimum retroreflectivity levels.
Notes: Note: The compliance date of June 13, 2014 applies only to the implementation and continued use of an assessment or management method that is designed to maintain regulatory and warning sign retroreflectivity at or above the minimum retroreflectivity levels in Table 2A-3. Agencies are expected to add signs other than regulatory or warning to their method as resources allow, per the footnote to the Compliance Date Table (I-2).
<number>

## Slide 15: Do guide signs and street name signs still have to meet the minimums?
Yes. The standards for minimum retroreflectivity requirements still apply to guide signs. The compliance date for guide signs (including street name signs) have been eliminated. However, agencies are expected to add these signs to their method as resources allow.
Notes: <number>

## Slide 16: More Information
MUTCD Website: http://mutcd.fhwa.dot.gov
Nighttime Visibility Website: http://www.fhwa.dot.gov/retro
    Regulations/Standards
    Technical Guidance
    Implementation Tools
    Frequently Asked Questions
    Research
Notes: <number>
Here are some sources that you can easily access to gain further information on retroreflectivity.
(Recommend handing out copies of the summary brochure: http://safety.fhwa.dot.gov/roadway_dept/retro/sa07020/sa07020.pdf
at any live presentation.)
Note: This is a first draft. For review purposes only.